## Slide 1
Syllabus of Embedded System
Unit 4: Embedded System Design Using VHDL (5 Hrs)
4.1 Introduction to VHDL
4.2 Different modeling styles in VHDL for combinational and sequential circuits
4.3 Data types in VHDL
4.4 Sub program and Packages
4.5 VHDL realization for combinational and sequential circuits

## Slide 2
Introduction to VHDL
VHDL, or Very High-Speed Integrated Circuit Hardware Description Language, was developed in early 1980s.
It becomes an IEEE standard in 1987 (IEEE 1076).
It provides a standardized way to describe and simulate the behavior of digital circuits before their implementation.
It can describe complex digital logic at various levels of abstraction.

## Slide 3
Introduction to VHDL
Key benefits includes:
High Level Abstraction: Digital circuits can be modeled in various levels.
Simulation before Implementation: Circuits can be verified through simulation.
Hardware Portability: Can be synthesized for different target devices.
Concurrent Design: Supports concurrent operations, aligning with nature of digital circuits.

## Slide 4
Introduction to VHDL
Basic Blocks of a VHDL program:
Entity: Defines external interface, specifying the input and output ports
Architecture: Defines the internal working of the entity
Package: Defines global elements such as data types, constants, and functions
Configuration: Allows designers to bind entities with their corresponding architecture.
Library: Defines various design units

## Slide 5
Introduction to VHDL
Structure of an Entity:
entity entity_name is
port (
signal_name1 : mode type;
signal_name2 : mode type
);
end entity_name;

## Slide 6
Introduction to VHDL
Structure of an Architecture:
architecture architecture_name of entity_name is
{architecture_declarative_part}
begin
{conc_stment}
end architecture_name;

## Slide 7
Introduction to VHDL
Basic language elements:
Identifiers: Names used to represent various elements in VHDL.
Data Objects in VHDL: Used to hold values of a specified type and are created using object declaration.
Data types: They define the nature and behavior of the values that can be assigned to variables, signals and other elements within a design.
Operators: They allow designers to perform various operations on data objects such as signals, variables and constants.

## Slide 8
Introduction to VHDL
Rules for Identifiers:
Starting Characters must be a letter (A-Z or a-z)
Can include letters, digits and underscores.
Two consecutive underscores and identifier that end with underscore are not allowed.
VHDL is case insensitive.
Comments in VHDL start with - - and continue until the end of the line.

## Slide 9
Introduction to VHDL
Data Objects in VHDL:
Constant: Holds a fixed value that cannot change during the simulation
constant <name>:<type>:=<value>;
Variable: holds a value, which can be changed during the execution of a process.
variable <name>:<type>:=<initial_value>;
Signal: They are used for communication between different processes or between different parts of a design.
signal <name>:<type>:=<initial_value>;
File: They allows reading from or writing to an external file during simulation.
file <name>:<type> is <external_file>;

## Slide 10
Introduction to VHDL
Predefined Data Types:

## Slide 11
Introduction to VHDL
User Defined Data Types:
Scalar Types: Represent single values or variables that store only A value at a time.
type TrafficLight is (Red, Green, Yellow);
Composite Types: Allow for the grouping of multiple values into a single data structure
type IntArray is array (0 to 7) of integer;
Access Types: Access types in VHDL are analogous to pointers

## Slide 12
Test bench
A testbench is an program written in VHDL that surrounds your actual hardware design. Unlike your main design, it does not get converted into hardware (gates). Instead, it acts as a "virtual tester“
Generates input signals.
Applies them to the Design Under Test (DUT)
Observes the output to check for correctness

## Slide 13
Test bench
The standard procedure for building Testbench
Empty Entity
Component Declaration
Signal Declaration
DUT(Design Under Test) Instantiation
Clock Generation (if design is sequential)
Stimulus Process

## Slide 14
VHDL programs
Test bench for AND gate
Library ieee;
Use ieee.std_logic_1164.all;
entity and_gate_tb is
end and_gate_tb;
architecture arc_and_tb of and_gate_tb is
component and_gate
port (
a,b : in std_logic;
c : out std_logic
);
end component;
signal sig_a : std_logic := '0';
signal sig_b : std_logic := '0';
signal sig_c : std_logic;
begin
u1: and_gate port map (
a => sig_a,
b => sig_b,
c => sig_c
);
atb : process
begin
sig_a <= '0'; sig_b <= '0';
wait for 100ps;
sig_a <= '0'; sig_b <= '1';
wait for 100ps;
sig_a <= '1'; sig_b <= '0';
wait for 100ps;
sig_a <= '1'; sig_b <= '1';
wait for 100ps;
wait;
end process;
end architecture arc_and_tb;

## Slide 15
VHDL programs
Test bench for OR gate
Library ieee;
Use ieee.std_logic_1164.all;
entity or_gate_tb is
end or_gate_tb;
architecture arc_or_tb of and_or_tb is
component or_gate
port (
a,b : in std_logic;
c : out std_logic
);
end component;
signal sig_a : std_logic := '0';
signal sig_b : std_logic := '0';
signal sig_c : std_logic;
begin
u1: or_gate port map (
a => sig_a,
b => sig_b,
c => sig_c
);
otb : process
begin
sig_a <= '0'; sig_b <= '0';
wait for 100ps;
sig_a <= '0'; sig_b <= '1';
wait for 100ps;
sig_a <= '1'; sig_b <= '0';
wait for 100ps;
sig_a <= '1'; sig_b <= '1';
wait for 100ps;
wait;
end process;
end architecture arc_or_tb;

## Slide 16
VHDL programs
Test bench for Half-adder gate
Library ieee;
Use ieee.std_logic_1164.all;
entity ha_gate_tb is
end ha_gate_tb;
architecture arc_ha_tb of and_ha_tb is
component ha_gate
port (
a,b : in std_logic;
c,s : out std_logic
);
end component;
signal sig_a : std_logic := '0';
signal sig_b : std_logic := '0';
signal sig_c : std_logic;
signal sig_s : std_logic;
begin
u1: ha_gate port map (
a => sig_a,
b => sig_b,
c => sig_c,
s => sig_s
);
hatb : process
begin
sig_a <= '0'; sig_b <= '0';
wait for 100ps;
sig_a <= '0'; sig_b <= '1';
wait for 100ps;
sig_a <= '1'; sig_b <= '0';
wait for 100ps;
sig_a <= '1'; sig_b <= '1';
wait for 100ps;
wait;
end process;
end architecture arc_ha_tb;

## Slide 17
VHDL programs
VHDL Code for D-flip flop(rising edge)
library ieee;
use ieee.std_logic_1164.all;
entity risingedge_dflipflop is
port(
q : out std_logic;
clk :in std_logic;
d :in std_logic
);
end risingedge_dflipflop;
architecture behavioral of risingedge_dflipflop is
begin
process(clk)
begin
if(rising_edge(clk)) then
q <= d;
end if;
end process;
end behavioral;
D
Q
clk

## Slide 18
VHDL programs
VHDL Code for Testbench of D-flip flop(rising edge)
library ieee;
use ieee.std_logic_1164.all;
entity tb_risingedge_dflipflop is
end tb_risingedge_dflipflop;
architecture behavioral of tb_risingedge_dflipflop is
component risingedge_dflipflop
port(
q : out std_logic;
clk : in std_logic;
d : in std_logic
);
end component;
signal clk_tb : std_logic := '0';
signal d_tb : std_logic := '0';
signal q_tb : std_logic;
constant CLK_PERIOD : time := 10 ns;
begin
uut: RisingEdge_DFlipFlop port map (
Q => q_tb,
Clk => clk_tb,
D => d_tb
);
clk_process : process
begin
clk_tb <= '0';
wait for CLK_PERIOD/2;
clk_tb <= '1';
wait for CLK_PERIOD/2;
end process;
stim_proc: process
begin
wait for 20 ns;
d_tb <= '1';
wait for 20 ns;
d_tb <= '0';
wait for 15 ns;
d_tb <= '1';
wait for 10 ns;
wait;
end process;
end Behavioral;

## Slide 19
VHDL programs
VHDL Code for JK-flip flop(rising edge)
library ieee;
use ieee.std_logic_1164.all;
entity risingedge_jkflipflop is
port(
j,k : out std_logic;
clk :in std_logic;
d :in std_logic
);
end risingedge_jkflipflop;
architecture behavioral of risingedge_jkflipflop is
signal q_s : std_logic;
begin
process(clk)
begin
J
Q
clk
K
if(rising_edge(clk)) then
if(j=‘0’ and k=‘0’) then
q_s <= q_s;
elsif (j=‘1’ and k=‘0’) then
q_s<= ‘1’;
elsif (j=‘0’ and k=‘1’) then
q_s<=‘0’;
elsif (j=‘1’ and k=‘1’) then
q_s<= not q_s;
endif;
end if;
end process;
q<=q_s;
end behavioral;

## Slide 20
VHDL programs
VHDL Code for Testbench for JK-flip flop(rising edge)
library ieee;
use ieee.std_logic_1164.all;
entity tb_risingedge_jkflipflop is
end tb_risingedge_jkflipflop;
architecture sim of tb_risingedge_jkflipflop is
component risingedge_jkflipflop
port(
j, k : in std_logic;
clk : in std_logic;
q : out std_logic
);
end component;
signal j_tb : std_logic := '0';
signal k_tb : std_logic := '0';
signal clk_tb : std_logic := '0';
signal q_tb : std_logic;
constant clk_period : time := 10 ns;
begin
uut: risingedge_jkflipflop
port map (
j => j_tb,
k => k_tb,
clk => clk_tb,
q => q_tb
);
clk_process: process
begin
clk_tb <= '0';
wait for clk_period/2;
clk_tb <= '1';
wait for clk_period/2;
end process;
stim_proc: process
begin
wait for 10 ns;
j_tb <= '1'; k_tb <= '0';
wait for clk_period;
j_tb <= '0'; k_tb <= '0';
wait for clk_period;
j_tb <= '0'; k_tb <= '1';
wait for clk_period;
j_tb <= '1'; k_tb <= '1';
wait for clk_period * 3;
j_tb <= '0'; k_tb <= '1';
wait for clk_period;
wait;
end process;
end sim;

## Slide 21
VHDL programs
VHDL Code for sequence detection (1001)
D
C
B
A
Init

## Slide 22
VHDL programs
VHDL Code for sequence detection (1001)
Init
A
B
D
C

## Slide 23
VHDL programs
VHDL Code for sequence detection (1001)
library ieee;
use ieee.std_logic_1164.all;
entity seq_1001 is
port (
clock: in std_logic;
reset: in std_logic;
seq_in: in std_logic;
detec_out: out std_logic
);
end seq_1001;
architecture behavioral of seq_1001 is
type moore_fsm is (init, a, b, c, d);
signal c_st, n_st: moore_fsm;
begin
process(clock,reset)
begin
if(reset='1') then
c_st <= init;
elsif(rising_edge(clock)) then
c_st <= n_st;
end if;
end process;
process(c_st,seq_in)
Begin
case(c_st) is
when init =>
detec_out <= '0';
if(seq_in='1') then
n_st <= a;
else
n_st <= init;
end if;
when a =>
detec_out <= '0';
if(seq_in='0') then
n_st <= b;
else
n_st <= a;
end if;

## Slide 24
VHDL programs
VHDL Code for sequence detection (1001)
when b =>
detec_out <= '0';
if(seq_in='0') then
n_st <= c;
else
n_st <= a;
end if;
when c =>
detec_out <= '0';
if(seq_in='1') then
n_st <= d;
else
n_st <= init;
end if;
when d =>
detec_out <= ‘1';
if(seq_in='1') then
n_st <= a;
else
n_st <= b;
end if;
end case;
end process;
end behavioral;

## Slide 25
VHDL programs
VHDL Code for sequence detection (1001)
library ieee;
use ieee.std_logic_1164.all;
entity seq_1001_tbis
end tb_seq_1001;
architecture behavior of seq_1001_tb is
component seq_1001
port(
clock : in std_logic;
reset : in std_logic;
seq_in : in std_logic;
detec_out : out std_logic
);
end component;
signal clock : std_logic := '0';
signal reset : std_logic := '0';
signal seq_in : std_logic := '0';
signal detec_out : std_logic;
constant clock_period : time := 10 ns;
begin
uut: seq_1001 port map (
clock => clock,
reset => reset,
seq_in => sequence_in,
detec_out => detec_out
);
clock_process :process
begin
clock <= '0';
wait for clock_period/2;
clock <= '1';
wait for clock_period/2;
end process;
stim_proc: process
begin
seq_in <= '0';
reset <= '1';
wait for 30 ns;
reset <= '0';
wait for 40 ns;
seq_in <= '1';
wait for 10 ns;
seq_in <= '0';
wait for 10 ns;
seq_in <= '1';
wait for 20 ns;
seq_in <= '0';
wait for 20 ns;
seq_in <= '1';
wait for 20 ns;
seq_in <= '0';
wait;
end process;
end;

## Slide 26
VHDL programs
Package
package package_name is
type my_type is array (0 to 7) of std_logic;
function my_function (x : integer) return integer;
end package package_name;
package body package_name is
function my_function (x : integer) return integer is
begin
return x + 1;
end function;
end package body package_name;

## Slide 27
VHDL programs
Package
library ieee;
use ieee.std_logic_1164.all;
package clk is
type clk_type is ('0','1');
function rising_edge (signal s: clk_type) return boolean;
end clk;
package body clk is
function rising_edge (signal s: clk_type)
return boolean is
begin
if (s'event) and (s='1') and (s'last_value='0') then
return true;
else
return false;
end if;
end rising_edge;
end package body clk;