## Slide 1
Syllabus of Embedded System
Unit 5: Communication Protocols (3 Hrs)
5.1 Serial Communication: UART, SPI, I2C
5.2 Wireless Communication: Bluetooth, ZigBee, Wi-Fi, LoRa, GSM/GPRS
5.3 Networking: TCP/IP Basics in Embedded Systems

## Slide 2
Communication Protocols
Standardized sets of rules and digital message formats that enables information exchange between devices.
Acts as a common language that ensures data transmission is orderly, accurate, and secure.
Governs the process of sending and receiving data between devices in a two-way communication exchange.

## Slide 3
Communication Protocols
Device Interoperability
Data integrity
System Efficiency
Scalability
Key roles of communication protocols

## Slide 4
Serial Communication (UART, SPI, I2C)
UART, or Universal Asynchronous Receiver/ Transmitter, is a physical circuit in a microcontroller or single integrated circuit (IC) that is used to implement serial communication between devices in an embedded system.
UART, data is sent over the bus in the form of a packet. A packet consists of a start bit, data frame, a parity bit, and stop bits.
UART, supports bidirectional data transmission, including half-duplex and full-duplex operations.
UART doesn’t use a clock signal

## Slide 5
Serial Communication (UART, SPI, I2C)
UART with data bus

## Slide 6
Serial Communication (UART, SPI, I2C)
UART frame format

## Slide 7
Serial Communication (UART, SPI, I2C)
Advantages of UART
Simple and cost-effective
Reliable Communication
Wide Usage
Applications of UART
Debugging
Peripheral Interfaces
Embedded Systems

## Slide 8
Serial Communication (UART, SPI, I2C)
Serial Peripheral Interface (SPI) is synchronous serial communication protocol.
Designed for high-speed, efficient communication.
It operates in a master-slave architecture and supports full-duplex communication.
Synchronized with a clock signal, which can operate on either the rising or falling edge of the clock cycle.

## Slide 9
Serial Communication (UART, SPI, I2C)
SPI configuration with master and a slave
Clock (SCLK) : Clock signal is generated by the master device and is used to synchronize data transfer between the master and the slave.

## Slide 10
Serial Communication (UART, SPI, I2C)
SPI configuration with master and a slave
Chip Select (CS) : The chip select signal, typically active low, is used by the master to select a specific slave device for communication.

## Slide 11
Serial Communication (UART, SPI, I2C)
SPI configuration with master and a slave
Master Out Slave In (MOSI) : This data line transmits data from the master to the slave.

## Slide 12
Serial Communication (UART, SPI, I2C)
SPI configuration with master and a slave
Master In, Slave Out (MISO) : This data line transmits data from the slave to the master.

## Slide 13
Serial Communication (UART, SPI, I2C)
Communication Process
Clock Synchronization
Data Transmission
Slave Selection
Multiple Slave Setup

## Slide 14
Serial Communication (UART, SPI, I2C)
SPI Mode 0, CPOL = 0, CPHA = 0: CLK idle state = low, data sampled on rising edge and shifted on falling edge.

## Slide 15
Serial Communication (UART, SPI, I2C)
SPI Mode 1, CPOL = 0, CPHA = 1: CLK idle state = low, data sampled on the falling edge and shifted on the rising edge.

## Slide 16
Serial Communication (UART, SPI, I2C)
SPI Mode 2, CPOL = 1, CPHA = 1: CLK idle state = high, data sampled on the falling edge and shifted on the rising edge.

## Slide 17
Serial Communication (UART, SPI, I2C)
SPI Mode 3, CPOL = 1, CPHA = 0: CLK idle state = high, data sampled on the rising edge and shifted on the falling edge.

## Slide 18
Serial Communication (UART, SPI, I2C)
Advantages of SPI
High-speed communication
Full-duplex Operation
Simple Hardware Requirement
Support for multiple Slaves
Applications of SPI
Memory Devices
Sensors
Display Modules
Communication Peripherals

## Slide 19
Serial Communication (UART, SPI, I2C)
Inter-Integrated Circuit Protocol, is a widely used two wire interface in embedded systems.
I2C allows multiple masters and slaves to share a single bus.
Its synchronous, half-duplex design minimizes wiring complexity.
There are only wires: Serial Data (SDA) and Serial Clock (SCL). Thus, also known as Two Wire Interface.

## Slide 20
Serial Communication (UART, SPI, I2C)
Generalized I2C connection diagram

## Slide 21
Serial Communication (UART, SPI, I2C)
Communication Process
Start Condition
Addressing
Data Transfer
Stop Condition

## Slide 22
Serial Communication (UART, SPI, I2C)
Frame format

## Slide 23
Serial Communication (UART, SPI, I2C)
Advantages of I2C
Simplified Wiring
Supports Multiple Devices
Synchronous Data Transfer
Built-in Acknowledgement
Applications of I2C
Sensor Integration
Display Communication
Memory Modules
Embedded Systems

## Slide 24
Wireless Communication: Bluetooth, ZigBee, Wi-Fi, LoRa, GSM/GPRS
Best for: Direct-to-smartphone connectivity and simple cable replacement.
Design Advantage: Native support on almost all modern mobile devices. You don’t need a gateway to talk to a phone.
Latency: Optimized for short bursts; has very fast "wake-to-connect" times (~3ms).
Embedded Tip: Use BLE 5.0+ features like Coded PHY if you need extra range at the cost of data rate, or 2M PHY for higher throughput.

## Slide 25
Wireless Communication: Bluetooth, ZigBee, Wi-Fi, LoRa, GSM/GPRS

## Slide 26
Wireless Communication: Bluetooth, ZigBee, Wi-Fi, LoRa, GSM/GPRS
Best for: Large-scale sensor networks (e.g., 50+ light switches or temperature sensors).
Design Advantage: Superior Self-Healing Mesh. If one node fails, data automatically reroutes. It is much more robust for "whole-house" or industrial floor coverage than BLE.
Integration Challenge: Requires a Gateway (Hub) to connect to the Internet or a smartphone.
Embedded Tip: Ensure you use a "Full Function Device" (FFD) for mains-powered nodes to act as routers, and "Reduced Function Devices" (RFD) for battery-powered end-nodes.

## Slide 27
Wireless Communication: Bluetooth, ZigBee, Wi-Fi, LoRa, GSM/GPRS

## Slide 28
Wireless Communication: Bluetooth, ZigBee, Wi-Fi, LoRa, GSM/GPRS
Best for: High-bandwidth applications like security cameras or devices that must connect directly to the Cloud without a hub.
Power Challenge: The "Keeping Alive" overhead of TCP/IP is taxing. It is difficult to run a Wi-Fi device on a coin-cell battery for long periods.
Security: Requires WPA2/WPA3 implementation, which is more resource-heavy for the MCU than Zigbee’s AES-128.
Embedded Tip: If battery life is critical but Wi-Fi is required, use Wi-Fi 6 (802.11ax) modules that support Target Wake Time (TWT), which allows the device to sleep for long periods.

## Slide 29
Wireless Communication: Bluetooth, ZigBee, Wi-Fi, LoRa, GSM/GPRS

## Slide 30
Feature | Bluetooth Low Energy (BLE) | Zigbee | Wi-Fi (802.11 b/g/n/ax)
Standard | IEEE 802.15.1 | IEEE 802.15.4 | IEEE 802.11
Data Rate | 1 Mbps to 2 Mbps | 250 Kbps | 11 Mbps to 10 Gbps+
Power Consumption | Ultra-Low (Months/Years) | Very Low (Months/Years) | High (Days/Weeks)
Network Topology | Star, Point-to-point, Mesh | Mesh, Star, Tree | Star (Access Point)
Max Nodes | ~20–30 (Star); 32k (Mesh) | 65,000+ | ~250 per Access Point
Indoor Range | ~10–30 meters | ~10–100 meters | ~50–100 meters
Primary Use | Wearables, Peripherals | Smart Home, Industrial | Video, Web, Cloud
Wireless Communication: Bluetooth, ZigBee, Wi-Fi, LoRa, GSM/GPRS

## Slide 31
Wireless Communication: Bluetooth, ZigBee, Wi-Fi, LoRa, GSM/GPRS
Best for: Battery-powered sensors in remote areas (e.g., soil moisture, tank levels).
Design Advantage: Extremely high receiver sensitivity allows signals to travel through buildings or even underground. You can build your own Private Network with a single gateway and zero monthly fees.
Duty Cycle Limits: In many regions (like the EU), you are legally restricted to a 1% duty cycle (e.g., transmitting for only 36 seconds per hour).
Embedded Tip: Choose your Spreading Factor (SF) carefully. A higher SF increases range but also increases "Time-on-Air," which drains the battery faster and risks packet collisions.

## Slide 32
Wireless Communication: Bluetooth, ZigBee, Wi-Fi, LoRa, GSM/GPRS

## Slide 33
Wireless Communication: Bluetooth, ZigBee, Wi-Fi, LoRa, GSM/GPRS
Best for: Mobile applications that move across cities or countries where you cannot install your own gateways.
Design Advantage: "Always-on" connectivity. Unlike LoRa, which is mostly "fire and forget" for small packets, GPRS allows for a persistent TCP/IP connection.
Power Challenge: GSM modules (like the SIM800 series) can pull 2A current spikes during transmission. You must design your power supply with large decoupling capacitors (e.g., 1000µF+) to prevent MCU burnouts.
Embedded Tip: For modern designs, look into LTE-M or NB-IoT modules. They offer cellular coverage with significantly lower power consumption than traditional 2G/3G.

## Slide 34
Wireless Communication: Bluetooth, ZigBee, Wi-Fi, LoRa, GSM/GPRS
GSM Module

## Slide 35
Feature | LoRa / LoRaWAN | GSM (2G) / GPRS
Network Type | LPWAN (Unlicensed) | Cellular (Licensed)
Range | 2–5 km (Urban), 15 km+ (Rural) | Virtually unlimited (Cell tower based)
Data Rate | 0.3 Kbps to 50 Kbps | ~30 Kbps to 115 Kbps
Power Consumption | Ultra-Low (Years on battery) | High (Needs large battery/mains)
Subscription Cost | None (Private) or Low (Public) | Monthly SIM data plan required
Hardware Cost | Medium ($3–$10 per module) | Higher ($10–$25 per module)
Primary Use | Remote sensors, Smart agriculture | Asset tracking, Remote monitoring
Wireless Communication: Bluetooth, ZigBee, Wi-Fi, LoRa, GSM/GPRS

## Slide 36
Networking: TCP/IP Basics in Embedded Systems
Key benefits includes:
High Level Abstraction: Digital circuits can be modeled in various levels.
Simulation before Implementation: Circuits can be verified through simulation.
Hardware Portability: Can be synthesized for different target devices.
Concurrent Design: Supports concurrent operations, aligning with nature of digital circuits.